## Slide 1: Optimal Joint Offloading and Wireless Scheduling for Parallel Computing with Deadlines
Xudong Qin* Weijian Xu† Bin Li*
*Dept. of Electrical, Computer and Biomedical Engineering, University of Rhode Island, Rhode Island, USA
†Information Engineering College, Jimei University, Xiamen, China

## Slide 2: Real-time Mobile Applications
Real-time video analysis
Low latency requirements
Low energy consumption
Intensive computation requirements
Real-time language translation
Notes: With the rapid growth of Artificial Intelligence (AI) technology, there is a strong need for real-time mobile applications such as real-time video analysis and real-time language translation. Those kinds of applications are faced with some difficult challenges, such as low energy consumption for mobile users, low latency and intensive computations requirements. In order to design algorithms to meet those challenges, we studied the joint offloading and wireless scheduling for parallel computing with deadlines.

## Slide 3: System Model
Mobile users
Access point
Edge servers
User 1
User 2
User N
Notes: Here is the system model. We have N mobile users, one access point and some powerful edge servers.
Parallel computing
Applications. A world trade center there are people around the world need to use the real-time translation service to communicate with each other. i.e. the real-time translation
Applications runs in parallel manners. For example, real-time translation 1. capture the image , 2. image recognition 3. natural language processing
Basic System setup:
𝑁 mobile users;
One access point (AP);
Some powerful edge servers;

## Slide 4: System Model (Cont’)
where is the maximal allowable drop rate for user , is the total number of packets that can be processed in frame . are the packets that perform local computation and are the transmission part.
Each user has dynamic and heterogeneous computing demands with strict time slots deadline.
Local computation
Transmission to edge server
Drop packets
In time frame ,
packets can be processed
0
T slots
Mobile User
packets
Energy Consumption:
Time frame
Notes: Each user has dynamic and heterogeneous computing demands with strict time slots deadline. We group consecutive time slots into a frame.
At the beginning of each frame, there are A_n[kT] packets arriving at user n. Upon arrival, we split the arrival into two parts. One part perform local computations and the other part perform wireless transmissions. If there are still packets available at the end of frame, we drop the remaining packets.
Our object is to minimize the average energy consumption for each mobile user. (local computations and wireless transmissions)
Each user 𝑛 has dynamic and heterogeneous computing demands with strict 𝑇 time slots deadline. We group 𝑇 consecutive time slots into a frame.
At the beginning of each frame, there are A_n[kT] packets arriving at user n. Upon arrival, we split the arrival into two parts. One part perform local computations and the other part perform wireless transmissions. If there are still packets available at the end of frame, we drop the remaining packets.
Our object is to minimize the average energy consumption for each mobile user. (local computations and wireless transmissions)

## Slide 5: A Motivating Example
Local-First Offloading and Scheduling (LFOS) Algorithm
Arriving packets are processed at mobile device first
Remaining parts are transmitted to edge server
Edge-First Offloading and Scheduling (EFOS) Algorithm
Arriving packets are transmitted to edge server first
Remaining parts are processed at mobile device
Notes: First let’s take a look at a simple motivation example. There are two heuristic algorithm. LFOS algorithm and EFOS algorithm.
LFOS: the arriving packets are processed at mobile device first, then the remaining parts are transmitted to edge server.
EFOS: the arriving packets are processed at edge server first, then the remaining parts are processed at mobile device.

## Slide 6: A Motivating Example (Cont’)
Policy | User | t=0 | t=1 | t=2 | t=3 | t=4 | t=5
LFOS | 1 |  |  |  |  |  | 
 | 2 |  |  |  |  |  | 
EFOS | 1 |  |  |  |  |  | 
 | 2 |  |  |  |  |  | 
Better Choice | 1 |  |  |  |  |  | 
 | 2 |  |  |  |  |  | 
In each slot, a mobile device can process 1 packet with 7 watt energy consumption;
In each slot, a mobile device can transmit 2 packets with 4 watt energy consumption;
Only one user can transmit packet within one slot.
2 mobile users
Access point
Edge servers
System setup: slots, users, at time each user has 6 packets waiting to be processed.
6 packets
Notes: In this example, we assume that there are 2 mobile users, one access point and some edge servers.
Let’s compare the performance of LFOS and EFOS with the better choice.

## Slide 7: A Motivating Example (Cont’)
Policy | User | t=0 | t=1 | t=2 | t=3 | t=4 | t=5
LFOS | 1 | 3, 11 |  |  |  |  | 
 | 2 | 5, 7 |  |  |  |  | 
EFOS | 1 | 3, 11 |  |  |  |  | 
 | 2 | 5, 7 |  |  |  |  | 
Better Choice | 1 | 4, 4 |  |  |  |  | 
 | 2 |  |  |  |  |  | 
In each slot, a mobile device can process 1 packet with 7 watt energy consumption;
In each slot, a mobile device can transmit 2 packets with 4 watt energy consumption;
Only one user can transmit packet within one slot.
2 mobile users
Access point
Edge servers
System setup: slots, users, at time each user has 6 packets waiting to be processed.
Packets remaining
Energy consumption
Notes: In time slot 0, user 1 is allowed for both local computation and wireless transmission. User 2 is allowed for local computation only.

## Slide 8: A Motivating Example (Cont’)
Policy | User | t=0 | t=1 | t=2 | t=3 | t=4 | t=5
LFOS | 1 | 3, 11 | 0, 11 |  |  |  | 
 | 2 | 5, 7 | 4, 7 |  |  |  | 
EFOS | 1 | 3, 11 | 0, 11 |  |  |  | 
 | 2 | 5, 7 | 4, 7 |  |  |  | 
Better Choice | 1 | 4, 4 | 2, 4 |  |  |  | 
 | 2 |  |  |  |  |  | 
In each slot, a mobile device can process 1 packet with 7 watt energy consumption;
In each slot, a mobile device can transmit 2 packets with 4 watt energy consumption;
Only one user can transmit packets within one slot.
2 mobile users
Access point
Edge servers
System setup: slots, users, at time each user has 6 packets waiting to be processed.
Packets remaining
Energy consumption

## Slide 9: A Motivating Example (Cont’)
Policy | User | t=0 | t=1 | t=2 | t=3 | t=4 | t=5
LFOS | 1 | 3, 11 | 0, 11 |  |  |  | 
 | 2 | 5, 7 | 4, 7 | 1, 11 |  |  | 
EFOS | 1 | 3, 11 | 0, 11 |  |  |  | 
 | 2 | 5, 7 | 4, 7 | 1, 11 |  |  | 
Better Choice | 1 | 4, 4 | 2, 4 | 0, 4 |  |  | 
 | 2 |  |  |  |  |  | 
In each slot, a mobile device can process 1 packet with 7 watt energy consumption;
In each slot, a mobile device can transmit 2 packets with 4 watt energy consumption;
Only one user can transmit packet within one slot.
2 mobile users
Access point
Edge servers
System setup: slots, users, at time each user has 6 packets waiting to be processed.
Packets remaining
Energy consumption

## Slide 10: A Motivating Example (Cont’)
Policy | User | t=0 | t=1 | t=2 | t=3 | t=4 | t=5
LFOS | 1 | 3, 11 | 0, 11 |  |  |  | 
 | 2 | 5, 7 | 4, 7 | 1, 11 | 0, 7 |  | 
EFOS | 1 | 3, 11 | 0, 11 |  |  |  | 
 | 2 | 5, 7 | 4, 7 | 1, 11 | 0, 4 |  | 
Better Choice | 1 | 4, 4 | 2, 4 | 0, 4 |  |  | 
 | 2 |  |  |  | 4, 4 |  | 
In each slot, a mobile device can process 1 packet with 7 watt energy consumption;
In each slot, a mobile device can transmit 2 packets with 4 watt energy consumption;
Only one user can transmit packet within one slot.
2 mobile users
Access point
Edge servers
System setup: slots, users, at time each user has 6 packets waiting to be processed.
Energy consumption
Packets remaining

## Slide 11: A Motivating Example (Cont’)
Policy | User | t=0 | t=1 | t=2 | t=3 | t=4 | t=5
LFOS | 1 | 3, 11 | 0, 11 |  |  |  | 
 | 2 | 5, 7 | 4, 7 | 1, 11 | 0, 7 |  | 
EFOS | 1 | 3, 11 | 0, 11 |  |  |  | 
 | 2 | 5, 7 | 4, 7 | 1, 11 | 0, 4 |  | 
Better Choice | 1 | 4, 4 | 2, 4 | 0, 4 |  |  | 
 | 2 |  |  |  | 4, 4 | 2, 4 | 
In each slot, a mobile device can process 1 packet with 7 watt energy consumption;
In each slot, a mobile device can transmit 2 packets with 4 watt energy consumption;
Only one user can transmit packet within one slot.
2 mobile users
Access point
Edge servers
System setup: slots, users, at time each user has 6 packets waiting to be processed.
Packets remaining
Energy consumption

## Slide 12: A Motivating Example (Cont’)
Policy | User | t=0 | t=1 | t=2 | t=3 | t=4 | t=5
LFOS | 1 | 3, 11 | 0, 11 |  |  |  | 
 | 2 | 5, 7 | 4, 7 | 1, 11 | 0, 7 |  | 
EFOS | 1 | 3, 11 | 0, 11 |  |  |  | 
 | 2 | 5, 7 | 4, 7 | 1, 11 | 0, 4 |  | 
Better Choice | 1 | 4, 4 | 2, 4 | 0, 4 |  |  | 
 | 2 |  |  |  | 4, 4 | 2, 4 | 0, 4
In each slot, a mobile device can process 1 packet with 7 watt energy consumption;
In each slot, a mobile device can transmit 2 packets with 4 watt energy consumption;
Only one user can transmit packet within one slot.
2 mobile users
Access point
Edge servers
System setup: slots, users, at time each user has 6 packets waiting to be processed.
Energy
consumption
Packets remaining

## Slide 13: A Motivating Example (Cont’)
Policy | User | t=0 | t=1 | t=2 | t=3 | t=4 | t=5
LFOS | 1 | 3, 11 | 0, 11 |  |  |  | 
 | 2 | 5, 7 | 4, 7 | 1, 11 | 0, 7 |  | 
EFOS | 1 | 3, 11 | 0, 11 |  |  |  | 
 | 2 | 5, 7 | 4, 7 | 1, 11 | 0, 4 |  | 
Better Choice | 1 | 4, 4 | 2, 4 | 0, 4 |  |  | 
 | 2 |  |  |  | 4, 4 | 2, 4 | 0, 4
In each slot, a mobile device can process 1 packet with 7 watt energy consumption;
In each slot, a mobile device can transmit 2 packets with 4 watt energy consumption;
Only one user can transmit packet within one slot.
2 mobile users
Access point
Edge servers
System setup: slots, users, at time each user has 6 packets waiting to be processed.
Policy | LFOS | EFOS | Better choice
Average Energy consumption for each user(watt) | 4.5 | 4.25 | 2
A better choice can save energy consumption up to 55.6% compared to LFOS.

## Slide 14: Algorithm Design
We introduce a virtual queue to keep track of the amount of packets that are dropped.
Virtual queue arrival:
packets drop
Virtual queue
Virtual queue service:
service is generated,
where
Virtual queue dynamics:
where
Then the average drop rate of user meets the requirement if its virtual queue is stable (c.f. [1, Definition 2.2] ).
[1] M. Neely, Stochastic network optimization with application to communication and queueing systems. Morgan & Claypool, 2010
Notes: Virtual queue that

## Slide 15: Joint Offloading and Scheduling Algorithm
Joint Offloading and Scheduling (JOS) algorithm
,
where
,
,
is some parameter,
Proposition 1: The JOS algorithm with any achieves close to the optimal energy consumption at the expense of the mean virtual queue-length growing with .
Strongly coupled
Nonlinear

## Slide 16: Algorithm Implement Roadmap
In JOS algorithm, the offloading decisions and wireless scheduling decisions are strongly coupled, which make it hard to implement
Consider one time slot deadline setup, we build decoupled joint offloading and scheduling (DJOS) algorithm for the case with one time slot deadline.
Based on the insight of one time slot DJOS, we developed DJOS for the general case.
Decoupled Joint Offloading and Scheduling (DJOS) algorithm
Wireless scheduling decisions
Offloading decisions

## Slide 17: Wireless Scheduling Decisions (1 Time Slot)
Calculate
Calculate
Calculate
User
User
User
Step 2:
Choose user for both wireless transmission and local computation, the rest users() only perform local computations
Step 3:
and are defined as follows:
Only local computation
Compute weight
Both local computation and wireless transmission
Compute weight
Step 1:

## Slide 18: Offloading Decisions(1 Time Slot)
For user that is allowed for both wireless transmission and local computations
For users that are allowed for local computations only
, and are defined as follows:

## Slide 19: General Case (T Time Slots)
Wireless scheduling decisions :
Wireless scheduling decisions are obtained by solving the following optimization problem:
where are the wireless scheduling decisions, denote the maximum number of wireless transmissions that are allowed for user in frame .
Offloading Decision:
The offloading decisions for each user are similar with the case with one time slot
complexity
User 1: schedule 3 time slots
User 2: schedule 2 time slots
slots

## Slide 20: Simulation Setup
users;
Maximal allowable drop rate ;
All users suffer from i.i.d ON-OFF channel fading;
Local computation energy consumption watt;
Wireless transmission energy consumption watt;
Local processing rate
The case with one time slot deadline | The case with three time slot deadline
Transmission rate 5 when the channel is ON | Transmission rate 4 when the channel is ON
The case with one time slot deadline | The case with three time slot deadline
Transmission rate 5 when the channel is ON | Transmission rate 4 when the channel is ON
Where denotes number of arriving packets and denotes the probability that have arrivals.

## Slide 21: Simulation Results (1 Time Slot Deadline)
The case with one time slot deadline
Figure (a) implies that all users satisfy the maximum allowable drop rate
Figure (b) shows that our proposed DJOS algorithm significantly saves the energy compared to LFOS
Figure (c) studies the impact of parameter M

## Slide 22: Simulation Results (3 Time Slots Deadline)
The case with three time slots deadline
Figure (a) implies that all users satisfy the maximum allowable drop rate
Figure (b) shows that our proposed DJOS algorithm significantly saves the energy compared to LFOS
Figure (c) studies the impact of parameter M

## Slide 23: Conclusions & Future work
We developed the joint offloading and scheduling (JOS) algorithm;
We developed the decoupled joint offloading and scheduling (DJOS) algorithm for the case with one time slot deadline;
We further developed the decoupled joint offloading and scheduling (DJOS) algorithm for general case;
Low-complexity implementation for the decoupled joint offloading and scheduling (DJOS) algorithm.

## Slide 24: Thank you! Q&A